## Slide 1
An Investigation Into Advanced Life Support system for Mars
Thursday 9th February, 10.30 AM
Chemical Engineering
Design Projects 4
Red Planet Recycle

## Slide 2: Outline
Design Outlook
Design brief
Stages of Design
Criteria & Constraints
Water treatment
Considered technologies
Selection procedure
ISS overview
Air Treatment
CO2 Removal
H20 Generation
O2 Generation
Red Planet Recycle

## Slide 3
Design Outlook
Design Brief
Your consulting company has been hired by the Mars Exploration Consortium, represented by Drs. Sarkisov and Valluri. The objective of the consortium is to build a space station on Mars, capable of a continuous support of a 10 member crew. It has been planned that a re-supply mission should return to Mars every 18 months, with the main resources re-supplied being water, oxygen and food. With the current cost of the re-supplement estimated at £1 M/kg, there is a clear need for intensive onsite recycling of the resources, including water, air and waste. Your company has been hired to develop an integrated recycling solution, with an objective to minimize the weight of the re-supplement cargo. Other technologies that should be explored along with the recycling, include collection and purification of water on Mars and local production of food stock (high protein vegetables etc). The primary source of energy for the Martial station will be provided by a nuclear reactor with up to 50 MWe capacity.
Red Planet Recycle

## Slide 4
Stages of design
We have identified 3 key stages of the design:
Resource requirements assuming no recycling or utilisation of local sources
Resource requirements with recycling introduced
Resource requirements with recycling introduced and utilisation of local resources. Investigation into unconventional technologies
Design Outlook
Red Planet Recycle

## Slide 5
Using previous isolated systems as examples the essential resources that must be controlled in a life support system are:
Water
Air
Food
Waste
Thermal energy
Biomass
The last three require control but no resupply on the Mars space station, therefore these are not considered at this stage of design.
Stage 1
Design Outlook
Red Planet Recycle

## Slide 6
Resource requirements
Total Water Requirement |  |  | 
Drinking | Hygiene* | Safety | Total
[kg] | [kg] | [kg] | [kg]
17472 | 92345 | 27454.25 | 137271.25
Total Air Requirement |  |  |  | 
N2 | O2 | CO2 | Safety | Total
[kg] | [kg] | [kg] | [kg] | [kg]
0 | 4599 | 0 | 1149.75 | 5748.75
Calorific requirement |  | 
Standard | Safety | Total
[MJ] | [MJ] | [MJ]
57.3 | 14.325 | 71.625
Total Oxygen | Total Water | Total Resupply Weight | Total Resupply Cost
[kg] | [kg] | [kg] | [£Million]
5748.75 | 137271.25 | 143020 | 143020
(Flynn et al., 2004)
Design Outlook
Red Planet Recycle

## Slide 7
Design Outlook…
Stage 1 | Stage 2 | Stage 3
Design Outlook
Red Planet Recycle

## Slide 8
Stage 2
Introducing recycling processes to the Mars space station in order to minimise the resupply requirements
Of the three focus resources identified in stage one, only two can effectively be recycled. These are:
Water
Air
Design Outlook
Red Planet Recycle

## Slide 9
Water
Treatment
Red Planet Recycle

## Slide 10
Assumptions
All consumed water requires recycling
Assuming NASA standard water composition
Water
Treatment
Red Planet Recycle

## Slide 11
Design Basis
Stage 1
Water
Waste water
(ppm)
Treated water
(ppm)
Ammonia 55 calcium 0.9
chlorine 229 phosphate 134 sulphate 80 Nitrate <100 sodium 150 potassium 133 magnesium 1.5 TOC >11
Ammonia 0.05 calcium 30
chlorine 200 phosphate N/A sulphate 250 Nitrate 10 sodium N/A potassium 340 magnesium 50 TOC <0.5
Flowrate 200.6 kg/day
M.Flynn (1998)
Water
Treatment
Red Planet Recycle

## Slide 12
Criteria & Constraints
Applicability
Reliability
Modularity
Resupply
But in general we look for the technology to be;
Lightweight and economical, able to recover a high percentage of waste water and operate with minimal consumables . Moreover the technology has to have sufficiently available data.
Water
Treatment
Red Planet Recycle

## Slide 13: ?
Criteria & Constraints
Technology | Applicability | Reliability | Modularity | Resupply
VPCAR |  |  |  | 
DOC |  |  |  | 
Electrocoagulation |  |  |  | ?
Microorganism based |  | - | - | -
ISS |  |  |  | 
Membrane |  |  |  | 
Advanced oxidation |  | - | - | -
Ecocyclet |  | - | - | -
UV treatment |  | - | - | -
Water
Treatment
Red Planet Recycle

## Slide 14: ?
Criteria & Constraints…
Technology | Applicability | Reliability | Modularity | Resupply
VPCAR |  |  |  | 
DOC |  |  |  | 
Electrocoagulation |  |  |  | ?
Microorganism based |  | - | - | -
ISS |  |  |  | 
Membrane |  |  |  | 
Advanced oxidation |  | - | - | -
Ecocyclet |  | - | - | -
UV treatment |  | - | - | -
Water
Treatment
Red Planet Recycle

## Slide 15: ?
Final Selection
 | DOC | EC | ISS | Membranes
Resupply (kg/18 months) | 50 | Unknown | 1032 | 0
No. of independent units | 3 | 1* | 4 | 3*
Feed streams | 2 | 1 | 2 | 1
Recovery rate (%) | 96 | - | 99 | 90
Maintenance | Unknown | - | 50 days | >18 months
 | DOC | EC | ISS | Membranes
Resupply (kg/18 months) | 50 | Unknown | 1032 | 0
No. of independent units | 3 | 1* | 4 | 3*
Feed streams | 2 | 1 | 2 | 1
Recovery rate (%) | 96 | - | 99 | 
Maintenance | Unknown | - | 50 days | >18 months
Water
Treatment
Red Planet Recycle

## Slide 16: ?
 | DOC | EC | ISS | Membranes
Resupply (kg/18 months) | 50 | Unknown | 1032 | 0
No. of independent units | 3 | 1* | 4 | 3*
Feed streams | 2 | 1 | 2 | 1
Recovery rate (%) | 96 | - | 99 | 90
Maintenance | Unknown | - | 50 days | >18 months
 | DOC | EC | ISS | Membranes
Resupply (kg/18 months) | 50 | Unknown | 1032 | 0
No. of independent units | 3 | 1* | 4 | 3*
Feed streams | 2 | 1 | 2 | 1
Recovery rate (%) | 96 | - | 99 | 
Maintenance | Unknown | - | 50 days | >18 months
Final Selection
Water
Treatment
Red Planet Recycle

## Slide 17: ?
DOC VS ISS
DOC requires a Re-supply of 4393 kg every 18 months
ISS Water Recovery System requires a Re-supply of 1032 kg every 18 months
Due to the difference in weight per Re-supply mission we have decided to choose to design the ISS Water Recovery System. However this is based on the 2007 paper where the recovery rate of the DOC system was 96%. If a more recent paper is able to determine a greater recovery rate the DOC system should be reconsidered for design.
Water
Treatment
Red Planet Recycle

## Slide 18
Water
Treatment
Process Flow

## Slide 19
Air
Treatment
Red Planet Recycle

## Slide 20: ?
Assumptions
The air treatment is split into three distinct processes: CO2 separation, CO2 consumption and O2 production
Assuming same composition of air as on Earth
Assume N2 is a buffer
Air
Treatment
Red Planet Recycle

## Slide 21: ?
Design Basis
CO2 Separation
10 kg/day CO2
H20 Generation
8.4 kg/day O2
Air
Air
O2 Generation
Air
Treatment
Red Planet Recycle

## Slide 22
Process Flow
CO2 Separation
CO2
Air
Treatment
Red Planet Recycle

## Slide 23: ?
Criteria & Constraints
CO2 Separation
Air
Treatment
Technology | Applicability | Reliability | Modularity | Resupply | Safety
TSA |  |  |  |  | 
MEA Absorption |  |  |  |  | 
PSA |  |  |  |  | 
Sorbents |  |  |  |  | 
Red Planet Recycle

## Slide 24: ?
Criteria & Constraints
CO2 Separation
Air
Treatment
Technology | Applicability | Reliability | Modularity | Resupply | Safety
TSA |  |  |  |  | 
MEA Absorption |  |  |  |  | 
PSA |  |  |  |  | 
Sorbents |  |  |  |  | 
Red Planet Recycle

## Slide 25
Final Selection
Air
Treatment
 | TSA | PSA
Resupply (kg/18 months) | 0 | 0
Relative efficiency at low CO2 concentrations | High | Low
Relative capital cost | High | Low
Relative operating cost | Low | High
Recovery rate (%) | - | 95*
Maintenance (years) | 3-5 | 3-5
Red Planet Recycle

## Slide 26
Final Selection
Air
Treatment
 | TSA | PSA
Resupply (kg/18 months) | 0 | 0
Relative efficiency at low CO2 concentrations | High | Low
Relative capital cost | High | Low
Relative operating cost | Low | High
Recovery rate (%) | >95 | >95
Maintenance (years) | 3-5 | 3-5
Red Planet Recycle

## Slide 27
Final Selection
Air
Treatment
Red Planet Recycle

## Slide 28
Process Flow
H20 Generation
H2
From Electrolysis
Air
Treatment
Red Planet Recycle

## Slide 29
H20 Generation
RWGS
Sabatier
Bosch
Bosch-Boudouard
Air
Treatment
Red Planet Recycle

## Slide 30
Criteria & Constraints
Technology | Applicability | Reliability | Modularity | Resupply
RWGS |  |  |  | 
Sabatier |  |  |  | 
Bosch |  |  |  | 
Bosch-Boudouard |  | n/a |  | 
H20 Generation
Air
Treatment
Red Planet Recycle

## Slide 31
Technology | Applicability | Reliability | Modularity | Resupply
RWGS |  |  |  | 
Sabatier |  |  |  | 
Bosch |  |  |  | 
Bosch-Boudouard |  | n/a |  | 
Criteria & Constraints
H20 Generation
Air
Treatment
Red Planet Recycle

## Slide 32
 | Sabatier | RWGS
Resupply (kg/18 months) | 1334.2 | 2343.5
No. of independent units | 1 | 1
Feed streams | 2 | 2
Maintenance | Unknown | Unknown
Final Selection
Air
Treatment
Red Planet Recycle

## Slide 33: ?
Feasibility studies for CO2 treatment methods indicate that the Sabatier reaction is the best choice for “stage 2”.
Possibility of improving the process in “stage 3” by recovering hydrogen from the methane, as opposed to venting it to Mars. This would create a closed loop for both H2 and O2, meaning neither would need to be resupplied.
H20 Generation…
Air
Treatment
Red Planet Recycle

## Slide 34
Process Flow
O2 Generation
Sabatier
H20
Air
Treatment
Red Planet Recycle

## Slide 35: ?
Photocatalytic splitting
Thermolysis
Thermochemical cycles
Catalysis
Electrolysis
Laser
H20 Generation
Air
Treatment
Red Planet Recycle

## Slide 36
Technology | Applicability | Reliability | Modularity | Resupply
Photocatalytic |  | - | - | -
Thermolysis |  | - | - | -
Thermochemical Cycles |  | ? |  | 
Catalysis |  | ? |  | 
Laser |  | - | - | -
Bipolar Electrolysis |  |  |  | 
PEM Electrolyzer |  | - | - | -
Solid Oxide Electrolyzer |  | - | - | -
Criteria & Constraints
O2 Generation
Air
Treatment
Red Planet Recycle

## Slide 37
Technology | Applicability | Reliability | Modularity | Resupply
Photocatalytic |  | - | - | -
Thermolysis |  | - | - | -
Thermochemical Cycles |  | ? |  | 
Catalysis |  | ? |  | 
Laser |  | - | - | -
Bipolar Electrolysis |  |  |  | 
PEM Electrolyzer |  | - | - | -
Solid Oxide Electrolyzer |  | - | - | -
Criteria & Constraints
O2 Generation
Air
Treatment
Red Planet Recycle

## Slide 38: ?
Bipolar Electrolysis
Well developed technology
Reliable
Able to provide continuous supply of O2
Simple to operate
O2 Generation
Air
Treatment
Red Planet Recycle

## Slide 39
Process Flow
Air
Treatment
Red Planet Recycle

## Slide 40
Process Flow
O2 Generation
Sabatier
H20
Air
Treatment
Red Planet Recycle

## Slide 41
An Investigation Into Advanced Life Support system for Mars
Discussion!
Chemical Engineering
Design Projects 4
Red Planet Recycle